## Slide 1: MetaboPique
A High-Throughput Computational Workflow for Validating, Annotating, and Organizing MS/MS Spectra Derived from Biological Samples
ASMS 67th Conference on Mass Spectrometry and Allied Topics
June 2-6, 2019
Tytus D. Mak, Concepcion A. Remoroza, Meghan C. Burke, and Stephen E. Stein
Mass Spectrometry Data Center, National Institute of Standards and Technology, Gaithersburg, MD

## Slide 2
In the past several decades, few analytical platforms have proven to be as vital and versatile to so many fields as tandem mass spectrometry (MS/MS)
(Glish et al. 2003)
INTRODUCTION

## Slide 3
Tandem Mass Spectrometry
Biological Samples
Biomolecular Analysis
Glycomics
Lipidomics
Metabolomics
Proteomics
INTRODUCTION

## Slide 4: An Ideal Workflow
INTRODUCTION
Biological sample
LC-MS/MS
MS/MS Spectra
Unique Biomolecule A
Unique Biomolecule B
Unique Biomolecule D
Unique Biomolecule C
Nature Paper
Science Paper
NAS member
Nobel Prize

## Slide 5: A More Realistic Workflow
Biological sample 1
Biological sample 1
Biological sample 1
Biological sample 1
Biological sample 1
Biological sample 1
MS/MS Spectra
MS/MS Spectra
Biological sample 100
LC-MS/MS
MS/MS Spectra
Biological sample 1
Biological sample 99
…
INTRODUCTION
Chromatographic Deconvolution
Dereplication
Quality Control
Organization
Validated MS2 spectral library
Identification
Characterization
JASMS Paper

## Slide 6: MetaboPique: Overview
A collection of computational tools arranged in a logical workflow for automating the creation of a validated, annotated, and organized library of MS2 spectra acquired from biological samples
  Extract ion chromatograms (XICs) for the precursor m/z of MS2 spectra
  Evaluating XICs for gaussianness via non-linear least squares fitting
  Eliminate low quality MS2 spectra
  Cluster high quality MS2 spectra from the same analyte across all samples
    Intra-sample XIC clustering
    Inter-sample clustering, even with different sample preparation methods
  Adduct type and charge prediction of the precursor via brute-force combinatoric XIC analysis
METHODLOGY

## Slide 7: A Demonstration of MetaboPique
DEMONSTRATION
Untargeted LC-MS/MS data acquired during analysis of 4 technical replicate Chinese Hamster Ovary (CHO) cell 50% acetonitrile metabolite extract samples
Reverse phase chromatography was performed using a C18 column, 30-minute gradient with mobile phase A consisting of 0.1% formic acid in water, and mobile phase B 0.1% formic acid in acetonitrile
51,512 ESI+ MS2 spectra were collected across all 4 samples via data-dependent acquisition methods on a Thermo Orbitrap Fusion Lumos with an HCD normalized collision energy of 20
11,528 MS2 spectra were associated with 7,458 well-behaved (i.e. gaussian) XICs and organized into 3,397 spectral clusters
1,793 clusters (52.7%) were annotated with adduct information
  1,069 unambiguously annotated with a single adduct type and charge
  724 annotated with 2 or more adduct types
Notes:
  Each spectral cluster represents a unique analyte (i.e. potential metabolites) across all samples
  11.5K MS2 spectra represents an ~77% reduction of the initial 51.5K set

## Slide 8: MetaboPique: Spectral Clustering Based On XIC
For a given sample, all MS2 spectra originating from the same MS1 XIC are clustered
METHODLOGY
Spectrum 1:
  Precursor: 591.2065 m/z
  RT: 454s
Spectrum 2:
  Precursor: 591.2034 m/z
  RT: 459s
Spectrum 3:
  Precursor: 591.2051 m/z
  RT: 466s
Spectrum 4:
  Precursor: 591.2055 m/z
  RT: 490s
Spec1
Spec2
XIC:
Trace m/z: 591.2065 (initiated by Spectrum 1)
438s
483s
Spec4
Spec3
Gaussian Fitting:
Peak apex: 460s (mean)
Peak start: 438s (-3σ)
Peak end: 483s (+3σ)
460s

## Slide 9: Spectral Cluster 666.4837_1638.84
DEMONSTRATION
3 spectra clustered by 1 XIC originating from 1 replicate sample
MS2 precursors: 666.4836 m/z (1653s) , 666.4840 m/z (1630s) , 666.666.4836 m/z (1642s)
All MS2 Spectra

## Slide 10: MetaboPique: Merging Clusters
METHODLOGY
XIC clusters across multiple samples are merged by comparing their representative spectra via cosine similarity
Rep Spectrum
Rep Spectrum
Cosine Similarity
Sample 1
XIC Cluster
Sample 2
XIC Cluster

## Slide 11: Spectral Cluster 616.2701_380.22
3 spectra clustered across 3 XICs originating from 3 replicates
MS2 precursors: 616.2702 m/z (378s), 616.2701 m/z (380s), 616.2709 m/z (374s)
DEMONSTRATION
All MS2 Spectra

## Slide 12: MetaboPique: Adduct Type and Charge Prediction
METHODLOGY
Putative adduct XICs associated with the precursor XIC are extracted from the MS1 data
A Spearman’s rank correlation coefficient is used to evaluate peak shape similarity
Cluster 687.9804_259.13
1 spectrum from 1 XIC originating from 1 replicate
MS2 precursor m/z: 687.9804
Predicted Adduct type: [M+Na]1+
[M+Na]1+
687.9804 – Na + H = 665.9985
687.9804 – Na + H – H2O = 665.9985
[M+H]1+
[M-H2O+H]1+

## Slide 13: MetaboPique: Adduct Type and Charge Prediction
METHODLOGY
[M+Na]1+
A brute force combinatoric approach to adduct prediction
13 common ESI+ adducts are considered, generating 156 potential targets for XIC extraction
[M+H]1+
[M+K]1+
[M+NH4]1+
[M-H2O+H]1+
[M-2H]2+
[M+H+Na]2+
[M+H+K]2+
[M+3H]3+
[2M+H]1+
[2M+Na]1+
[2M+K]1+
[M+Na]1+
[M+H]1+
[M+K]1+
[M+NH4]1+
[M-H2O+H]1+
[M-2H]2+
[M+H+Na]2+
[M+H+K]2+
[M+3H]3+
[2M+H]1+
[2M+Na]1+
[2M+K]1+
687.9804 – H + Na =709.9624
[M+Na]1+
[M+H]1+
Precursor Adduct
Corroborating Adducts

## Slide 14: Cluster 608.3855_999.07
DEMONSTRATION
4 spectra clustered across 4 XICs originating from 4 fractions
All MS2 Spectra
MetaboPique: XIC & Inter-Sample Clustering + Adduct Prediction

## Slide 15: Cluster 608.3855_999.07
DEMONSTRATION
[M+NH4]1+
[M+H]1+
[M+Na]1+
Adduct type: [M+NH4]1+

## Slide 16
MetaboPique: Automated, High-Throughput, Intuitive
A streamlined computational workflow that simplifies the many complicated aspects of biological sample based spectral library creation
Utilizes MS1 information to the fullest:
  Quality assessment of MS2 spectra
  Clustering
  Adduct type prediction
A work in progress…collaborators?
CONCLUSIONS
tytus.mak@nist.gov

## Slide 17: Thanks!
Connie Remoroza
Meghan Burke
Adam Broerman
Kelly Telu
Arun Moorthy
Steve Stein
Bill Wallace

## Slide 18
IsoPique: Workflow
METHODLOGY
Biological sample 100
LC-MS/MS
Biological sample 1
Biological sample 99
…
Chromatographic Data
Chromatographic Data
Chromatographic Data
Elucidate XICs for all MS2 spectra
Evaluate XICs for Gaussianness via non-linear least squares
Extract isotopic XIC traces
Well-Behaved XICs
Monoisotopic m/z + charge state prediction
Isotope XICs
Annotated, validated,
XIC clustered MS2 spectra
Inter-Sample Superclustering
Superclustered
MS2 Spectra
Majority Spectrum creation

## Slide 19
IsoPique: Clustering Workflow
METHODLOGY
Inter-sample XIC clustering
Extract isotopic XIC traces