## Slide 1: Essential Elements of MS …
Steve Stein MS Data Center Chemical and Biochemical Reference Data Division Materials Measurement Lab NIST
Data Analysis

## Slide 2: Data Analysis
Data
  MS: Qualities, behavior, formats
  LC/MS: Complexity and dimensions
Analysis
  Algorithms: Mostly Proprietary
  Identity: How to Express Confidence
Notes: Amounts – determined as an ‘afterthought’
Cover significant basics and selected illustrations

## Slide 3: MS Data
Single stream of ions vs. time
  Detector: Electron multiplier or Ion image current
  A destructive ‘spectroscopy’
Two time ‘domains’
  Time converted to m/z
  Time converted to chromatographic component
Two ‘peaks’
  m/z and Chromatographic
m/z from time, Intensity from current
Charge (z) from isotope spacing

## Slide 4: MS Signals vs Time
Intensity
Noise
Notes: All event-counting detectors such as electron multipliers or photomultipliers produce signals that fluctuate, on average, proportional to the square root of the signal. This value is extracted from each chromatogram by using regions with relatively constant signal intensity. Nontrivial GC/MS data files always contain such regions, and fail-safe values are created for cases where it is not possible to find regions to establish noise. These regions are examined to find signals with multiple crossings of the local mean. A number of these regions are analyzed to determine the noise factor.

## Slide 5: Mass Spectra: Qual/Quan
Mass (m/z): Qualitative
  Measure chemical formula
    Elemental composition
  Provides Identification
  Accuracy depends on instrument class not ion source
Intensity: Quantitative
  MS1: variable
  MS2: relative intensities may be reproducible
  Variable, depends on ion source

## Slide 6: 2 Varieties of ‘Mass Spectra’
MS1
  Intact ions (‘evaporate’ from solution, mostly)
MS2
  Fragments of ions – depends on structure
  MS/MS, Tandem MS, MSn, PSD, …
  Wide or Narrow m/z range

## Slide 7: MS1
Ion Profile from the ‘ion source’
Variable : ‘matrix effects’ and source instability
ESI, MALDI, ‘Ambient Methods’
Proteins and Their Fragments
  Resolved 13C Isotopes (< 30 kD, 250 AA residues)
    Benefits from resolution and sensitivity
  Unresolved Ions ( > 30 kD, lower if heterogeneous)
    Benefits from sensitivity only

## Slide 8: MS2 – Wide precursor m/z range
Multiple ions co-fragment
  In-source (all ions fragment)
  MSE, m/z range, Wide Band Ion Trap, …
Different ions require different energies to fragment
  m/z, charge state, structure

## Slide 9: MS2 – Select Individual Ions
Energy Dependence
  Strong: Collision Cell (Beam-Type, QQQ) – Ions gain internal energy as decelerated
  Weak: Ion Trap – Ions heated in small increments until they fragment
  Fixed: Post-source decay (MALDI)– like Collision Cell but cannot vary energy
Molecular ‘fingerprints’ for Individual Ions
  Determined by chemical structure
  Save in Library
Predictability
  Small molecules (organic molecules) - NO
  Peptides, including glycopeptides – Yes
Proteins and large fragments (research)
  Small fragments will be isotopically resolved

## Slide 10: Mass Spectra are Reproducible
O’Neal et al. Anal. Chem. 1951
NIST 2012
A mass spectrum is a property of an ion
Notes: .. Why do I say that <next slide>

## Slide 11: Energy Dependence
[M+H+K]2+
30
35
40
CollisionEnergy Setting

## Slide 12
V1/2 product = precursor abundance
Resistance to fragmentation for 2500 tryptic peptide ions
QQQ Results for 25 Protein Digests JASMS 2009 20, p.469

## Slide 13: Diving into the Data
Chromatogram
“Ion Map”
Ion Clusters

## Slide 14
Signals From Various Sources
Tryptic digest of egg white

## Slide 15: Ion Components in a Protein Digest

## Slide 16
Signal Variability
Relative Peptide Ion Intensities In Successive Runs
Yeast Tryptic Digest
Piening B.D. et al J. Proteomics Res. 2006, 5, 1527

## Slide 17
Yeast Tryptic Digest
Piening B.D. et al J. Proteomics Res. 2006, 5, 1527
Successive Runs & First/Last Pair

## Slide 18: Huge Differences Between Labs
Black: Successive Runs
Blue: Other Lab
NIH/NCI/CPTAC Interlab Studies, 2010
Same Sample, Instrument, Method

## Slide 19: Raw Data
Data stored permanently on disk
  Is filtered from original signal – intensity vs. time
    Converted and stored as intensity vs m/z
    Classes of output
      Profile data – time to m/z only
      ‘Centroiding’ – identifies and adds signals for individual m/z peaks
  Files are big and growing in size: 500 MB / run not uncommon
    Inconvenient for Internet
    Title 21 CFR part 11 – keep for inspection with software?
  Web-based, raw data repositories struggling
    Size and annotation are major problem
Each vendor has its own format(s)
  Access requires vendor involvement
    Application Programming Interface
    Translator to Standard Format (mzML – proteomics driven)
  Third party software is limited – for experts only
    Proprietary algorithms

## Slide 20: Data Analysis Software
Proteomics Based
  Bottom Up (Infer Protein Structure from Fragments)
    X!Tandem, OMSSA, … (Public) MASCOT, Sequest (Proprietary)…
      Complex software packages – ‘validation’
      Protein ‘assembly’, finds only what you are looking for
    Specialized Biotherapeutics software (how it works)
      Other peptides – disulfides
      Epitope mapping – H/D exchange
  MW from charge state envelopes (‘deconvolution’)
    Black box: Heterogeneity & signal strength effects
  Top Down
    Prosite by Kelleher’s group
Compare Data Files
  “Biomarker Discovery” – case/control
  Sample tagging (mass label on each sample)

## Slide 21
thresholds
Probably wrong
Probably
right
Probably right
Confirmed

## Slide 22
peptide.nist.gov
NISTMSQC: Library/Quality Metrics for LC-MS/MS data “Performance Metrics for Liquid Chromatography-Tandem Mass Spectrometry Systems in Proteomics Analyses”, Molecular & Cellular Proteomics, 9, 225, 2010

## Slide 23: Peptide Library Spectrum Search
Query
Spectrum
Library
(Consensus)
Spectrum
Hit
List
Score
Histogram
Spectrum List
Will Hold Spectra of Biologic Drug Components

## Slide 24: NIST Library Pipeline

## Slide 25: Final Thoughts
Masses and identities can be determined with amazing and increasing accuracy
  Just in time identities of biologic drug materials
Sensitivity is increasing, but so is variability
  High sensitivity needed for HCP, contaminants
  Not for structure elucidation
Proprietary software/formats dominate
  Changes with time and instrument